## Slide 1: Topic 1
Introduction to Computer

## Slide 2: The Computer Revolution
Progress in computer technology
  Moore’s Law
Makes novel applications feasible
  Auto pilot vehicle
  Cell phones
  Robotic arms
  Internet+
  ……
Computers are pervasive

## Slide 3: Classes of Computers
Desktop computers
  General purpose, variety of software
  Subject to cost/performance tradeoff
Embedded computers
  Hidden as components of systems
  Subject to power/performance/cost constraints
Server computers
  Network based
  High capacity, performance, reliability
  Range from small servers to building sized

## Slide 4: Where can we find Computers
Desktop, Laptop, hand held PC, …
Automotive
  Automatic Ignition Systems, Cruise, ABS, traction control, airbag release system…
Consumer Electronics
  TV, PDA, appliances, toys, cell phones, camera …
Industrial Control
  robotics, control systems …
Medical
  Infusion Pumps, Dialysis Machines, Prosthetic Devices, Cardiac Monitors, …
Networking
  wired and wireless routers, hubs, …
Office Automation
  fax, photocopiers, printers, scanners, …
Aerospace applications
  Flight-control systems, engine controllers, auto-pilots and passenger in-flight entertainment systems…
Defense systems
  Radar systems, fighter aircraft flight-control systems, radio systems, and missile guidance systems…

## Slide 5
Product: Hunter Programmable Digital Thermostat.
Microprocessor: 4-bit
by Daniel W. Lewis

## Slide 6
Product:Vendo V-MAX 720 vending machine.
Microprocessor: 8-bit Motorola 68HC11.
by Daniel W. Lewis

## Slide 7
Product: Sonicare Plus toothbrush.
Microprocessor: 8-bit Zilog Z8.
by Daniel W. Lewis

## Slide 8: Product: Miele dishwashers. Microprocessor: 8-bit Motorola 68HC05.
by Daniel W. Lewis

## Slide 9: Product: NASA's Mars Sojourner Rover. Microprocessor: 8-bit Intel 80C85.
by Daniel W. Lewis

## Slide 10
Product: CoinCo USQ-712 coin changer.
Microprocessor: 8-bit Motorola 68HC912.
by Daniel W. Lewis

## Slide 11: Product: Garmin Nüvi GPS Receiver Microprocessor: 32-bit.

## Slide 12: Product: Motorola i1000plus iDEN Multi-Service Digital Phone. Microprocessor: Motorola 32-bit MCORE.
by Daniel W. Lewis

## Slide 13: Product: Nintendo Wii Controller Microprocessor: IBM 32-bit Power RISC

## Slide 14: Product: Apple iPad Microprocessor: Apple A4, a 32-bit ARM RISC.

## Slide 15: Product: Apple iWatch Microprocessor: 32-bit Apple A6 and M7 Coprocessor

## Slide 16: Product: HUAWEI P20 Pro Microprocessor: 8 64-bit ARMv8-A, the same architecture as iPhone X
by Daniel W. Lewis

## Slide 17: Product: Sony Aibo ERS-110 Robotic Dog. Microprocessor: 64-bit MIPS RISC.
by Daniel W. Lewis

## Slide 18: Anatomy of a Computer
Output device
Input device
Input device
Network cable

## Slide 19: Opening the Box

## Slide 20: Inside the Processor (CPU)
Datapath: performs operations on data
Control: controls how data flows
Cache memory
  Small fast SRAM memory for immediate access to data

## Slide 21: Inside the Processor
AMD Barcelona: 4 processor cores

## Slide 22: Peripheral – Memory
Volatile main memory
  Loses instructions and data when power off
Non-volatile secondary memory
  Magnetic disk
  Flash memory
  Optical disk (CDROM, DVD)

## Slide 23: Peripheral – Networks
Communication and resource sharing
Local area network (LAN): Ethernet
  Within a building
Wide area network (WAN): the Internet
Wireless network: WiFi, Bluetooth

## Slide 24: Peripheral – others
(Source: Wikipedia.org)

## Slide 25: Together with Software
Application software
  Written in high-level language (HLL)
System software
  Operating System: service code
    Handling input/output
    Managing memory and storage
    Scheduling tasks & sharing resources
  Written in C and assembly
Hardware
  Processor, memory, I/O controllers

## Slide 26: Levels of Program Code
High-level language
  What we use
Assembly language
  What both we and computers can use
Machine instruction
  What computers use

## Slide 27: Levels of Program Code
High-level language
  Syntax is similar to English
  A translator is required to translate the program – compile
  Allows the user to work on the program logic at higher level

## Slide 28: Levels of Program Code
Assembly language
  Composed of assembly instructions
  An assembly instruction is a mnemonic representation of a machine instruction
  Assembly instruction must be translated before it can be executed – assembler
  Programmers need to work on the program logic at a very low level, hard to achieve high productivity.

## Slide 29: Levels of Program Code
Machine instruction
  A sequence of binary digits which can be executed by the processor
  Hard to understand, program, and debug for human being
From Wikipedia

## Slide 30: Technology Trends
Electronics technology continues to evolve
  Reduced cost
  Parallelism
  Low power
  Increased capacity and performance
(From Wikipedia)

## Slide 31: Technology Trends

## Slide 32: Power Trends
In CMOS IC technology
×1000
×30
5V1V in 15y, 15% off/generation
Hit the wall

## Slide 33: How to Measure Computer Performance?
Execution (response) time
  How long it takes to do a task
  Measure for PCs and embedded computers
Throughput
  Total work done per unit time
  Servers
We’ll focus on execution time for now

## Slide 34: Measuring Performance - Time
Elapsed time – for System Performance
  Total execution time to complete a task, including
    Processing, I/O, OS overhead, idle time, everything
  But doesn’t completely reflect computer’s performance if it focuses on better throughput
CPU time – for CPU Performance
  CPU execution time processing a task
    Exclude I/O time, time spent for other tasks
  Comprises user CPU time and system CPU time
    Hard to differentiate
  Different programs run with different CPU performance and system performance
    User must know what’s the desired performance metric

## Slide 35: Understanding Performance
Performance-related factors:
Algorithm
  Determines number of operations executed
Programming language, compiler, architecture
  Determine number of machine instructions executed per operation
Processor and memory system
  Determine how fast instructions are executed
I/O system (including OS)
  Determines how fast I/O operations are executed

## Slide 36: CPU Clocking
Operation of digital hardware governed by a constant-rate clock
Clock (cycles)
Data transfer and computation
Update state
Clock period

## Slide 37: CPU Time
Performance improved by
  Reducing number of clock cycles
  Increasing clock rate
Tradeoff we will face when designing the CPU

## Slide 38: CPU Time Example
Computer A: 2GHz clock, 10s CPU time
Designing Computer B
  Aim for 6s CPU time
  Can do faster clock, but causes 1.2 × clock cycles A
How fast must Computer B clock be?

## Slide 39: Instruction Count (IC) and Clock cycle Per Instruction (CPI)
Instruction Count for a program
  Determined by program, Instruction Set Architecture (ISA), and compiler
Cycles per instruction
  Determined by CPU hardware
  If different instructions have different CPI
    Average CPI, affected by instruction mix
How instructions related to performance?
Classic CPU
performance equation

## Slide 40: CPI Example
Computer A: Cycle Time = 250ps, CPI = 2.0
Computer B: Cycle Time = 500ps, CPI = 1.2
Same ISA
Which is faster, and by how much?
A is faster…
…by this much

## Slide 41: Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Tc
The BIG Picture

## Slide 42: Concluding Remarks
Classes and applications of computer
Cost/performance is improving
  Due to underlying technology development
Hierarchical layers of abstraction
  In both hardware and software
Execution time: the best performance measure
Power is a limiting factor
  Use parallelism to improve performance